## Slide 1
METAL SEGMENTATION FOR ARTIFACT REDUCTION
Projection-Domain vs Image-Domain Segmentation
A comparative study of two deep-learning approaches to segmenting metal
implants in CT / CBCT scans, with a hands-on U-Net implementation.
Presentation • Monday Review

## Slide 2
Agenda
What we'll cover today
The Problem
Why metal implants corrupt CT/CBCT images and why segmentation matters
Two Domains
Image-domain vs projection-domain metal segmentation
Paper 1 — CBCT Projection Domain
Synthetic-data U-Net for projection-domain segmentation (Agrawal et al.)
Paper 2 — CT Image Domain
Diffusion-based segmentation, DiffSeg (Xie et al.)
Head-to-Head Comparison
Which domain segments metal better, and why
My Implementation
U-Net based metal mask segmentation notebook — approach & results
2

## Slide 3
The Problem: Metal Artifacts in CT / CBCT
Why accurate metal segmentation matters
Metal implants (screws, plates, dental fillings, hip prostheses) are
high-density and cause severe artifacts:
Blooming, streaking and shading around metal regions
Obscured boundaries hinder diagnosis & dose planning
Metal Artifact Reduction (MAR) inpaints the metal trace —
but this requires accurate metal segmentation first
Manual segmentation is slow, subjective, and impractical
for thousands of CT/CBCT projections
Typical MAR Pipeline
1. Acquire CT / CBCT scan
2. Segment metal
(image domain or projection domain)
3. Mask / inpaint metal trace
in projections or sinogram
4. Reconstruct corrected image
Step 2 — metal segmentation — is the focus of both papers reviewed.
3

## Slide 4
Two Segmentation Domains
Where in the imaging pipeline does segmentation happen?
Image Domain
Segmentation is performed on the reconstructed 3D CT volume (axial slices), typically using HU-based thresholds or learned models on reconstructed images.
Operates on reconstructed slices (e.g. 512x512 HU volumes)
Simple thresholds (2500/3000 HU) are common baselines
Must be forward-projected back to sinogram/projection
space for projection-based MAR
Projection Domain
Segmentation is performed directly on the raw 2D X-ray projections (sinogram for CT, projections for CBCT) before reconstruction.
Operates directly on raw 2D projections / sinograms
No forward-projection step needed for MAR
Handles motion blur and out-of-FOV metal naturally
4

## Slide 5
Paper 1 — Projection-Domain Metal Segmentation (CBCT)
Agrawal, Hietanen & Sarkka, IEEE Access 2023
Synthetic Training via Monte Carlo Simulation
Real ground-truth metal labels are hard to obtain — boundaries
are unclear and there are hundreds of projections per scan
Solution: simulate metal-corrupted CBCT projections + ground
truth from 10 real metal-affected clinical scans (knee, wrist,
foot, ankle, palm, forearm)
Compares noisy (300-1400 photons/pixel) vs clean (5000
photons/pixel) simulations — noisy is cheaper & more realistic
Trains a modified U-Net (4 down/up blocks, instance norm) on
full-size projections + crops together for robustness
Key Results (10 clinical test scans)
94.8%
Mean DSC
Best model: Noisy (full+crops)
90.2%
Mean IOU
Noisy (full+crops)
90.5%
Mean DSC — CMAR
(threshold-based baseline)
0.51e-3
False positive rate
on 6 metal-free scans
Best result: Noisy simulation + full-size & cropped projections trained together significantly outperformed CMAR, MMAR, and consistency-check methods, especially for motion-affected and out-of-FOV metals.
5

## Slide 6
Paper 1 — Model & Training Pipeline
Modified U-Net trained purely on simulated CBCT projections
1
Reconstruct & Threshold
FDK reconstruction of real CBCT scans; metal segmented via global HU threshold (>=3400 HU), refined with median filter + dilation
2
Monte Carlo Simulation
Photon-transport simulation generates metal-only & metal-inserted projections (PENELOPE/Badal-style), with realistic noise
3
Modified U-Net Training
4 encoder + 4 decoder blocks, instance norm, trained on simulated full-size + cropped (474x370) projections; BCE loss
4
Binary Metal Trace Output
Sigmoid + 0.5 threshold gives the binary metal mask directly in the projection, ready for inpainting-based MAR
Network: U-Net variant — 16 to 256 channels, 3x3 conv + ReLU + instance norm, bilinear upsampling, skip connections, 1x1 output conv + sigmoid. Trained on a single RTX 2080 Ti, Adam optimizer, BCE loss, with stacked augmentations (flips, elastic deformation, noise, dropout).
6

## Slide 7
Paper 2 — Image-Domain Metal Segmentation (CT)
Xie et al., DiffSeg — BMC Medical Imaging 2024
Diffusion Probabilistic Model for Metal Masks
Operates on reconstructed axial CT slices (512x512), not raw
projections
DiffSeg = ResU-Net diffusion model + Conditional Dynamic
Coding (fuses mask + prior image) + GFParser (removes
high-frequency noise via learnable Fourier filter)
Trained on 100 patients (11,280 slices) with simulated metal
artifacts inserted into real artifact-free CT images
Validated on clinical artifact CT, CTPelvic1K, and physical
phantoms with known titanium rod geometry
Key Results (2,820 test slices)
95.45%
Mean DSC — DiffSeg
(best among all models)
97.89%
Accuracy — DiffSeg
84.19%
Mean DSC — T3000
threshold baseline
93.52%
Mean DSC — U-Net
(traditional baseline)
DiffSeg outperformed U-Net, Attention U-Net, R2U-Net & DeepLabV3+ on simulated, clinical, and phantom data (statistically significant, p<0.05 vs most models). Its smaller, tighter masks better preserve surrounding bone detail during MAR.
7

## Slide 8
Paper 2 — DiffSeg Architecture
Conditional dynamic coding + global frequency parser on a ResU-Net backbone
1
Artifact Simulation
Metal masks (dental fillings, screws, hip implants, coils) inserted into clean CT; beam hardening + Poisson noise simulated for realism
2
Diffusion Process
Forward process adds Gaussian noise to the segment label over T=1000 steps; ResU-Net learns to reverse it conditioned on the CT image
3
Dynamic Conditional Coding
Fuses current segmentation mask features with the original-image prior at multiple scales to focus on the metal region
4
GFParser
FFT-based learnable frequency filter removes high-frequency noise introduced by the conditional fusion, sharpening mask edges
Ablation impact: Removing both modules drops DSC to 93.56% (DiffSeg_1). Dynamic conditional coding alone gives 94.35% (+0.79%). Adding GFParser reaches the full 95.45% (+1.1% total) — each component contributes measurably.
8

## Slide 9
Head-to-Head Comparison
Projection-domain (CBCT) vs Image-domain (CT) metal segmentation
Aspect | Projection Domain (Paper 1) | Image Domain (Paper 2)
Modality / Data | CBCT, extremity scans (knee, wrist, ankle, foot) | CT, head/neck, chest, abdomen + phantoms
Model | Modified U-Net (CNN, supervised) | DiffSeg — diffusion model + ResU-Net
Training data | Purely synthetic (Monte Carlo simulation) | Simulated artifacts on 100 real patient CTs
Best DSC | 94.8% | 95.45%
Best Accuracy / IOU | IOU = 90.2% | ACC = 97.89%
vs Threshold baseline | CMAR (region-growing): DSC 90.5% | T3000 threshold: DSC 84.19%
Key strength | No forward projection needed; robust to motion, out-of-FOV metal, and voxel-size changes | Sharper, smaller masks; better detail near metal in NMAR correction
Inference cost | Single forward pass (fast, ~ms) | Diffusion sampling (~3 s/batch, DPM-Solver)
9

## Slide 10
VERDICT
Which Domain Segments Metal Better?
It depends on the goal — but projection-domain segmentation is the stronger choice for CBCT-based MAR pipelines, while image-domain (DiffSeg) wins on raw segmentation accuracy for reconstructed CT.
Projection Domain wins when...
Metal is out-of-FOV or scan has heavy motion artifact
(image-domain cannot segment what isn't reconstructed)
Pipeline needs direct integration into existing
projection-based MAR (no forward-projection step)
Real-time / single-pass inference is required
Image Domain (DiffSeg) wins when...
Highest raw DSC/Accuracy on reconstructed slices is
the priority (95.45% vs 94.8%)
Fine boundary detail and noise suppression matter
(GFParser removes high-frequency artifacts)
Sufficient compute is available for diffusion sampling
(~3s per batch)
10

## Slide 11
My Implementation — U-Net Metal Mask Segmentation
Task: build & train a U-Net to segment metal regions in CT slices
Approach
Dataset: 500 CT slices (512x512) with paired binary metal
masks, loaded as raw float32 arrays
Preprocessing: min-max normalization, resized to 128x128
(image: bilinear, mask: nearest-neighbour to keep it binary)
Model: lightweight U-Net — 2 encoder blocks (16->32 ch),
bottleneck (64 ch), 2 decoder blocks with skip
concatenation, 1x1 conv + sigmoid output
Training: 80/20 train-test split, Adam optimizer, binary
cross-entropy loss, 15 epochs
Image-domain task — directly comparable to DiffSeg
approach in Paper 2
Training Results
99.86%
Train accuracy
(epoch 15)
99.89%
Val accuracy
(epoch 15)
0.0040
Train loss (BCE)
(epoch 15)
0.0033
Val loss (BCE)
(epoch 15)
Sample input slice & ground-truth metal mask
Predicted mask vs ground truth (test sample)
11

## Slide 12
Implementation — Observations & Next Steps
Where this fits relative to the reviewed papers
Observations
Validation accuracy (99.89%) is very high but driven mainly
by background pixels — DSC/IOU on the metal class would
give a fairer picture (as both papers report)
Predicted mask is smoother / slightly larger than ground
truth — similar to over-segmentation seen with simple
threshold methods in Paper 2
128x128 downsampling may blur small or thin metal
structures; both papers avoid downsampling near metal
boundaries for this reason
A compact 2-level U-Net was sufficient for this dataset's
large, well-separated metal regions
Suggested Next Steps
Report DSC / IOU / sensitivity / specificity per the metrics
used in both papers for direct comparability
Compare against a fixed-threshold baseline (2500/3000 HU)
as done in Paper 2
Apply data augmentation (flips, elastic deformation) following
U-Net (Ronneberger et al.) and Paper 1's strategy
Evaluate on full-resolution slices / crops to preserve fine
metal boundaries, as recommended in Paper 1
Long term: extend to the projection domain (CBCT) using
simulated data, mirroring Paper 1's pipeline
12

## Slide 13
Summary
Both domains push U-Net beyond simple HU thresholds — DSC improved from ~84% (threshold) to ~95% (deep learning)
Projection-domain (Paper 1) is best suited to CBCT pipelines: motion-robust, handles out-of-FOV metal, single fast pass
Image-domain DiffSeg (Paper 2) achieves the highest raw segmentation accuracy via diffusion + frequency-domain refinement
My U-Net notebook implements the image-domain approach — a strong foundation to extend toward Paper 2's evaluation rigor
Thank you — questions welcome